# FITTING INSTRUCTIONS FOR GROWLER® COLD AIR INDUCTION UNIT

HOLDEN VT-VY V6 & V6 Supercharged

## Part # CAI031

Kit Includes			               Tools Required

1x Airbox Assembly                            Drill

(incl. box, lid & rewashable filter)    Phillips Screwdriver

3x Black Self-Tapping Screws	    8mm Socket

1x Metal Retaining Clip

1.	Remove the airflow meter. Remove the rubber sleeve and 	clamp from standard airbox and retain.

2.	Remove factory intake.

3.	Remove standard airbox by gently pulling up from its rubber 	mounts. Remove temp sensor from the lid of standard airbox 	and refit to pre-drilled hole in Growler® airbox, using metal 	retaining clip supplied.

4.	Disconnect rubber overflow tube from below radiator cap.

5.	Fit Growler® airbox by sliding radiator overflow bottle through hole in Growler® airbox. Reconnect rubber overflow tube then position Growler® airbox under radiator support bracket.

6.	Drill 3 holes in radiator support bracket & secure Growler® 	airbox using the 3 x black self-tapping screws supplied.

7.	Refit rubber sleeve and clamp to lid of Growler® airbox. Refit 	airflow meter ensuring directional arrow is pointing toward 	motor.

Don’t forget to keep the rewashable Big Mouth® Filter clean!

Please note that the engine computer in your vehicle may take up to several hundred kilometres to adjust to the increased airflow and produce the maximum effect.

( ENJOY THE DIFFERENCE (