# FITTING INSTRUCTIONS FOR COLD AIR INDUCTION UNIT

FORD FG 6cyl & V8

## Part # CAI036 (6cyl) & CAI037 (V8)

Kit Includes			           Tools Required

1x Air Dam			           Drill

1x Intake Cover                             Phillips Screwdriver

4x Black Self-Tapping Screws

1x Panel Filter

- Remove factory intake, retaining scrivet to re-fit.

- Remove top panel and grill, retaining scrivets to re-fit.

- Place air dam supplied under panel so that it sits snug under the panel opening. Screw in place with 2x black self-tapping screws supplied.

- Refit top panel and grille. Refit factory intake.

- Fit intake cover supplied to mouth of factory intake which will also cover hole in top panel. Note the V8 intake cover sits on the inside of the factory intake whereas the 6cyl adheres to the outside of the factory intake. (Remove protective cover from double-sided tape first – 6cyl only). Drill 2 holes and secure with remaining 2x black self-tapping screws supplied.

7.	For 6cyl only - remove restrictor out of air box lid port to 	motor – this is easily done by pulling it from the inside of 	the lid.

8.	Remove filter from plastic bag and fit to factory airbox.

Please note that the engine computer in your vehicle may take a minimum of 500 kilometres to adjust to the increased airflow and produce the maximum effect. Until computer has fully adjusted, hard acceleration may cause flat spot or hesitations. This is due to the extra airflow and the computer will adjust with driving.

( ENJOY THE DIFFERENCE (