# FITTING INSTRUCTIONS FOR COMPUTER COVER

## FORD BA – FG 6cyl & V8 & FORD Territory

### Part # CPC001

Kit Includes                                          Tools Required

1x Computer Cover                               Hacksaw Blade

3x Stainless Steel Allen Key Bolts           Bladed Screwdriver

4mm Allen Key

- Using a hacksaw blade, cut a slot in the top of each rivet head on the computer housing; this needs to be just enough to get a bladed screwdriver in to turn.

- Using a bladed screwdriver, unscrew each rivet (anti-clockwise) and discard.

- Fit cover supplied over computer housing.

- With the 4mm Allen key, affix cover in place using the 3x Allen key bolts supplied. Spray CRC to threads before screwing.

NB: Some models may have a switch attached to the computer mounting bracket – either remove and tuck in under computer cover or mark and cut computer cover accordingly.

( ENJOY THE DIFFERENCE (