# FITTING INSTRUCTIONS FOR DUAL ENGINE COVERS

## HOLDEN VT-VY V8 5.7 GENIII

### Part # DEC001 +

#### Kit Includes                                     Tools Required

2x Engine Covers                             10mm Socket

- Remove the original engine cover and retain the 4 bolts.

- From the underside of the original engine cover, remove the

4 brass/plastic fittings that serve as spacers.

- Place these 4 spacers on the original threaded shaft of the brackets on the engine so that the wider part of the spacer

is pointing downwards.

- If necessary, slightly bend the brackets (that hold the securing nuts) towards the exhaust manifold and the engine oil dipstick away from the motor, for clearance.

- Put dual engine covers in place and, using the 4 original bolts, secure and tension as required.

( ENJOY THE DIFFERENCE (