# FITTING INSTRUCTIONS FOR ENGINE COVERS

## FORD BA – FG BOSS V8

### Part # ECK001+

Kit Includes                                      Tools Required

1x Engine Cover			    4mm Allen Key

2x Tappet Covers		              Drill

1x Computer Cover			   13mm Spanner

10mm Spanner

1.	Remove radiator overflow bottle (2x 10mm bolts) & oil cap.

2.	Remove original engine cover (3x 4mm Allen key bolts).

3.	Remove the 3x washers and rubbers from the original engine 	cover and affix to engine cover supplied.

4.	Remove 2x 13mm bolts from the spark plug access point (driver’s side). Remove 1 x 13mm bolt from passenger’s side. Retain bolts.

5.	Fit tappet cover supplied and tension down with the original 	13mm bolts. Repeat on opposite side. Do not overtension.

6.	Replace radiator overflow bottle and oil cap.

7.	Fit engine cover supplied using the original 3x 4mm Allen key bolts. (The Allen key at rear of engine is held by a bracket and 8mm bolt to corner of manifold – loosen this bolt until cover fully fitted. This will help pull down engine cover when 8mm bolt is re-tensioned.)

8.	Fit computer cover supplied as per enclosed instructions.

NB: If the Big Mouth® cold air induction is fitted to vehicle (BA-BF), you may want more clearance to engine cover. Remove engine cover and rework bracket upwards. Refit engine cover.