# FITTING INSTRUCTIONS FOR INFILL PANEL

## HOLDEN VY & VZ SS UTE

### Part # VUP002

Kit Includes						Tools Required

1x Plastic Infill Panel					Phillips Screwdriver

7x Short Self-Tapping Screws			Drill

2x Brackets

1.	Remove rear number plate.

2.	Remove centre number plate light, pulling wires through as far as possible.

Disconnect bulb from light socket.

3.	The brackets provided are connected to the bottom of the panel to attach it to 	the vehicle. Ensure each bracket is evenly spaced, approx. 12cm from either 	end (note that this is a guide only – adjust to suit your vehicle). Position 	panel, lining up to match existing lines on rear bumperettes, noting that slight 	adjustment of bumperettes may be necessary once infill panel is completely 	fitted.

4.	Establish and mark where you will be attaching the 2 brackets; remove panel, 	drill holes in the panel and in the vehicle where marked. Secure brackets to 	the panel with 2 of the self-tapping screws provided.

5.	To secure the top of the panel to the vehicle, drill a hole in the panel and in 	the vehicle approx. 21cm to the left of the middle of the spare wheel release 	cutout.

6.	Reposition panel to vehicle; secure bottom brackets with 2 of the self-tapping

screws provided. Secure top with 1 of the self-tapping screws provided, 	ensuring number plate light wiring is accessible to refit light.

7.	Refit number plate light and reconnect bulb.

8.	Refit number plate, using the last 2 self-tapping screws provided.

( ENJOY THE DIFFERENCE (